## Slide 1
9th IAA International Planetary Defense Conference
Planetary Defense Activities in JAXA
M. Yoshikawa, M. Kasahara, A. Iwaki, R. Yoshida,
T. Miyoshi, H. Shinomiya, Y. Muto, M. Abe,
T. Okada, N. Ozaki, T. Saiki, Y. Shimaki,
H. Takeuchi, S. Tanaka, Y. Tsuda, K. Nishiyama,
N. Higashio, Y. Mimasu, T. Ikenaga, K. Kamiya,
H. Kurosaki, T. Yanagisawa, K. Nitta, Y. Sakurai,
S. Nakamura, S. Ohkawa, T. Iori, M. Fujimoto (JAXA)
May 6, 2025
Stellenbosch, Cape Town, South Africa
JAXA Planetary Defense Team
IAA-PDC-25-02-153

## Slide 2: Contents
JAXA's activities for planetary defense
2024 YR4:
Collision probability analysis
Deflection by Hayabusa2
2

## Slide 3: JAXA's activities for planetary defense
NEO observation at Bisei Spaceguard Center (BSGC)
Discovery of high-speed moving objects by new NEO search method
Observations
Past & current : Hayabusa, Hayabusa2, Hayabusa2 extended mission
Future : DESTINY+, Next Generation Sample Return mission, etc.
Participation in ESA's Hera mission
Cooperating with ESA on RAMSES
SMPAG, IAWN, PDC, Asteroid Day
International activities
Asteroid observation for citizen science (ex. APAON, Occultation obs., etc.)
Public events
Outreach
Symposiums/meetings/sessions related PD
Domestic activities
Orbit propagation
Orbit estimation
Collision analysis
Space Missions
Orbit analysis

## Slide 4
Observation facility
(Research and Development Directorate)
Mt.Nyukasa Observational facility
Chofu LEO Observational facility
Remote observation site at Siding Spring Observatory
Remote observation site at Zadko Observatory
1m telescope
0.5m telescope
・Built in 2000 and owned by the Japan Space Forum, it was transferred to JAXA in April 2017.
・The observation work is carried out by the Japan Spaceguard Association (NPO).
・Observation targets: Space debris, NEO (asteroids)
Bisei Spacegurad Center (BSGC)
(Space Tracking and Communications Center)
Asteroid observations in JAXA
2025/5/6
PDC2025
4

## Slide 5: Discovery of fast moving small objects
Provisional designation | Mag. at discovery | e | a (au) | i (deg) | Distance at discovery (au) | Abs. Mag.
2017 BK | 17.5 | 0.489 | 1.909 | 6.6359 | 0.051 | 24.0
2017 BN92 | 17.1 | 0.483 | 1.921 | 1.0734 | 0.014 | 25.6
2018 EZ2 | 18.2 | 0.510 | 1.951 | 4.9718 | 0.01 | 26.6
2018 FH1 | 18.7 | 0.177 | 0.938 | 3.5468 | 0.013 | 26.6
2018 PM10 | 18.3 | 0.427 | 1.780 | 9.2065 | 0.001 | 27.0
2018 RR4 | 18.0 | 0.621 | 2.637 | 3.1793 | 0.015 | 27.1
2018 UG3 | 19.4 | 0.423 | 1.662 | 6.1673 | 0.03 | 24.5
2019 GW1 | 17.5 | 0.114 | 0.934 | 13.2945 | 0.009 | 26.1
2019 GT19 | 18.2 | 0.370 | 1.273 | 7.7488 | 0.01 | 27.5
2019 QU4 | 18.1 | 0.332 | 1.426 | 10.1313 | 0.017 | 24.8
2020 FC2 | 18.5 | 0.398 | 1.644 | 6.8153 | 0.006 | 28.0
Discovered NEOs by the stacking method
by using small telescopes (~20cm)
We developed a stacking method to find fast moving small objects.
We assume various movements of a faint object and overlap the images to find it.
Experimental observation:

## Slide 6: NEO missions related to JAXA
Hayabusa (2003-2010)
Hayabusa2 (2014-2020)
DESTINY＋
Target : Phaethon
Launch 2028, flyby 2030
（Image credit：JAXA / A. Ikeshita）
flyby in 2026
NGSR
Next Generation small body Sample Return mission
Target : comets
Launch 2030'
Hayabusa2# (2020 ~ )
Itokawa
S-type, 530m
Hera (ESA)
Target : Didymos, Dimorphos
Launch 2024, arrival 2026
Rendezvous in 2031
arrived in 2005
arrived in 2018
Ryugu
C-type, 1000m
Torifune
S-type, 500m ?
1998 KY26
30m ? smaller?
?
?
JAXA provided TIRI.
RAMSES (ESA)
JAXA collaboration
Target : Apophis
JAXA's mission
JAXA collaboration
6

## Slide 7: Hayabusa2 Extended mission : Hayabusa2#
After Hayabusa2 returned the sample of Ryugu in Dec. 2020, we extended the mission for two more targets, (98943) Torifune (2001 CC21) and 1998 KY26.
（Image credit：JAXA）
# (SHARP) : Small Hazardous Asteroid Reconnaissance Probe
now
※ indicates the number of orbits around the Sun.
Relative velocity : 5km/s
High accuracy navigation is necessary.
Artist's illustration (by A. Ikeshita)
Asteroid size : ~30m or 11m?
(spin period : ~11 or 5min?)
The collision probability of such asteroids with the Earth is once in 100~200 years.
Torifune
7
Next presentation by T. Hirabayashi

## Slide 8: Hera / RAMSES collaborations
JAXA provided the thermal infrared camera (TIRI).
© ESA
・ Broadband (8-14 µm) and six narrow band (1µm width)
・FOV：13 x 10 deg
・Measurement of temperature and physical properties of the asteroid surface layer
Flight spare of TIRI for Hera
©ESA
Hera
RAMSES
© JAXA
© JAXA
JAXA is considering to provide followings:
Thermal infrared camera (TIRI)
Lightweight Solar Array Wing
Possible launch opportunities
Lightweight Solar Array Wing
TIRI
8
See the poster by T. Okada (IAA-PDC-25-02-176)

## Slide 9: Apophis observation from satellites
JAXA currently has no plans to launch a new satellite/spacecraft to the asteroid Apophis.
We are investigating the possibility of observing Apophis using existing satellites.
This is currently under consideration and no conclusion has been reached yet.
See the poster of T. Ikenaga (IAA-PDC-25-07-95)
9

## Slide 10
JAXA organized the "Asia-Pacific Asteroid Observation Network (APAON)" to effectively utilize telescopes in the Asia-Pacific region and contribute to planetary defense.
Asteroid observers in Japan are also organized into Japanese teams.
Promoting asteroid observation in this area
★
★
Distribution of ground observation networks.
Original illustration： by Timothy Spahr.
Asia-Pacific Asteroid Observation Network (APAON)
Dec. 2013 APAON was proposed at APRSAF※ and called for participation
2014 Introduced at IAWN and SMPAG meetings
Jan. 2015 Started observation campaign as test observation. Eleven countries and regions participated.
2018 Activity suspended.
2025 Attempting to restart
※:Asia-Pacific Regional Space Agency Forum

## Slide 11: Deep-space multi-object orbit determination system (DMOODS) = JAXA's software for the orbit determination of deep space mission
This system has the ability to simultaneously estimate the orbits of deep space probes and target celestial bodies:
For Hayabusa2 mission:
  The final approach phase to Ryugu
  The estimation of the gravity field of Ryugu
  The final guidance phase returning to the Earth
  Precise estimation of Ryugu's orbit
Developed a function to directly import asteroid observation data of ground-based telescopes.
Collision probability analysis for 2024 YR4
O-C rms: 9.404e-05 deg = 0.33 arcsec
We used the data published by the Minor Planet Center (MPC), and the orbit of 2024 YR4 was estimated.
11

## Slide 12: Collision probability analysis for 2024 YR4
JAXA's solution
Feb. 6, 2025
Col. prob. : 0.82%
Feb. 27, 2025
Col. prob. : 0.0%
Feb. 16, 2025
Col. prob. : 2.04%
The estimated probabilities were consistnet with those of by JPL and ESA.
12

## Slide 13: Collision probability analysis for 2024 YR4
JAXA's solution
Feb. 6, 2025
Col. prob. : 0.82%
Feb. 16, 2025
Col. prob. : 2.04%
In these simulations, the particles that collide with the Earth are not deleted after the collision.
13

## Slide 14: Deflection of 2024 YR4 by Hayabusa2
If we give up arriving at 1998 KY26, it is possible to direct Hayabusa2 to 2024 YR4 by changing the conditions of the two Earth swing-bys.
[Case1]
HYB2’s Earth swing-by (2027/12/7)
HYB2’s YR4 Impact (2028/9/10)
YR4’s Earth encounter (2032/12/22)
HYB2’s Earth swing-by (2028/6/7)
HYB2’s YR4 Impact (2028/11/23)
YR4’s Earth encounter (2032/12/22)
Case1
▶Earth Swing-by : 2027/12/07.0 UT
▶YR4 intercept : 2028/09/10.0 UT
▶Intercept Velocity: 16.14km/s
▶YR4 sun-lit phase : 12.8deg
(Near full-moon)
Case2
▶Earth Swing-by : 2028/06/07.0 UT
▶YR4 intercept : 2028/11/23.0 UT
▶Intercept Velocity: 10.80km/s
▶YR4 sun-lit phase : 128.0deg
(Crescent-moon)
[Case2]
We investigated whether it would be possible to change the orbit of YR4 using Hayabusa2, which is currently in flight.

## Slide 15: Deflection of 2024 YR4 by Hayabusa2
Case2
ε=1.0, deflection ΔV= 41.2mm/s
ε=2.0, deflection ΔV= 82.5mm/s
ε=3.0, deflection ΔV=123.7mm/s
ε=4.0, deflection ΔV=164.9mm/s
We investigated the changes in the velocity and the position of 2024 YR4, when Hayabusa 2 is collided with YR4.
Earth
3σ ellipse of nominal YR4 traj.
This calculation is based on the JAXA's solution on Feb. 6, 2025
The impact of Hayabusa2 to 2024 YR4 has the effect of shifting the YR4 orbit largely to the right on the B-plane.
Assumptions：
YR4: d~50m, ρ~2g/cm3
Hayabusa2: mass~500kg
Impact efficiency(ε) : 1 ~ 4
(DART : ε= 2.2 ~ 4.9)
[Case1]
B-plane Passage for Impact with ε=1.0,2.0,3.0,4.0
Case1
ε=1.0, deflection ΔV= 61.6mm/s
ε=2.0, deflection ΔV=123.3mm/s
ε=3.0, deflection ΔV=184.9mm/s
ε=4.0, deflection ΔV=246.6mm/s

## Slide 16: Deflection of 2024 YR4 by Hayabusa2
Earth and YR4
3σ ellipse of nominal YR4 traj.
▶ YR4’s Earth Impact Probability : 22.0%
ε=2.0
ε=3.0
▶ YR4’s Earth Impact Probability : 0.58%
▶ YR4’s Earth Impact Probability : 0.01%
We assumed a fictitious case, where 2024 YR4 collides with the Earth.
Assumptions：
YR4: d~50m, ρ~2g/cm3
Hayabusa2: mass~500kg
Impact efficiency(ε) : 2 or 3
YR4 orbit error becomes 1/10
Hayabusa2 can avoid the collision of 2024 YR4 with the Earth!
[Case1]
However, because Hayabusa2 is spacecraft for rendezvous, it is difficult to collide it with a small target object at high speed.

## Slide 17: Deep Space Constellation Concept
Many (for example, 12) spacecraft are put in an asteroid flyby cycler orbit (alternating asteroid flyby and Earth swing by).
Then, we can perform one NEO flyby per month (ΔV~10 m/s per year, which is feasible for micro/nano spacecraft) .
We can also visit to such a newly discovered asteroid like 2024 YR4!
New idea!
Earth Gravity Assist
Asteroid #1
Asteroid #2
Asteroid #3
Earth Departure
(Rideshare/
Dedicated launch)
Spacecraft 2
Asteroid #4
Spacecraft 3
Spacecraft 1
Rapid response flyby
Earth Gravity Assist
Asteroid #5
Multiple asteroid flybys
(in the loitering orbit)
（©JAXA）

## Slide 18: Summary
For the planetary defense, JAXA carries out a variety of activities, including observation, exploration, calculations, international and domestic responses, and outreach.
Orbit determination and Earth impact analysis for 2024 YR4 were carried out, and the obtained collision probability were almost consistent of those by NASA/ESA.
Using the currently operated Hayabusa2 spacecraft, we investigated the possibility of changing the orbit of 2024 YR4. The results showed that orbital change was theoretically possible. (However, since Hayabusa 2 is a rendezvous probe, it would be technically difficult to actually carry this out.)

## Slide 19: Thank you!