## Slide 1: Hypothetical Asteroid Impact Exercise
    Panel 1a: Notification of asteroid impact threat and early preparedness
Point of Contact: Terik Daly
terik.daly@jhuapl.edu

## Slide 2: Panel Objectives
Raise awareness about the nature of asteroid threats and challenges related to preparing for an effective international response
Awareness Raising
Hear international viewpoints about asteroid impact threats and potential ways of responding to them
International Views
Discuss ways of communicating with decision makers about a potential asteroid impact and options for responding to it
Decision Making
Expand perspectives of planetary defense specialists about how non-specialists perceive asteroid impact threats
Perception

## Slide 3: Meet the Presenters
NASA Headquarters & International Asteroid Warning Network
Kelly Fast
NASA JPL Center for Near-Earth Object Studies
Davide Farnocchia
NASA Ames Asteroid Threat Assessment Project
Lorien Wheeler
Technical University of Munich & Space Mission Planning Advisory Group on behalf of ESA
Detlef Koschny

## Slide 4
EXERCISE EXERCISE EXERCISE
It is 1 August 2024.

## Slide 5
It is 1 August 2024.

## Slide 6
Simulated Impact Threat Scenario
Notification by the International Asteroid Warning Network
(IAWN)
Kelly Fast, NASA
IAWN Coordinating Officer
9th IAA Planetary Defense Conference
Scenario date: 1 August 2024
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE

## Slide 7
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
The International Asteroid Warning Network (IAWN)
A worldwide collaboration recommended by the United Nations to detect, track, and physically characterize near-Earth objects
Signatories include scientific institutions, observatories, and independent astronomers involved in asteroid observations, orbit computation, and modeling
IAWN’s goal is to provide the most accurate and up-to-date information available on the impact potential and effects
Currently 69 signatories from over 28 countries
7

## Slide 8
Overview for NEO Threat Response
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
8

## Slide 9
NEO Observations to Impact Predictions
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
NEOCC – Near-Earth Object Coordination Centre
CNEOS – Center for Near Earth Object Studies
NEO position measurements from observatories worldwide
Minor Planet Center
Provides identification, designation, and initial orbit computation
ESA NEOCC
NASA CNEOS
Provide independent calculations of NEO orbits and potential impact information
Information made available to the public and to support follow-on observations by Earth-based and space-based facilities
9

## Slide 10
IAWN shall warn of predicted impacts exceeding a probability of 1% for all objects characterized to be greater than 10 meters in size* and notify:
Chair, Space Mission Planning Advisory Group (SMPAG)
United Nations Office for Outer Space Affairs (UNOOSA)
  UNOOSA will notify UN Member States
IAWN signatories will also notify and work with their own governments according to their own national policies, as applicable.
  * Roughly equivalent to an absolute magnitude of 28 if only brightness data can be collected
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
10
IAWN Notification
Notes: Rationale: Impact probabilities greater than 1 per cent are rare yet warrant awareness of possible effects. Most objects greater than 10 meters in size could have some effects (air blast and pieces) that could reach the Earth’s surface. IAWN is compelled to warn populations if bodies will have effects that reach the ground. Setting threshold at 1 per cent is a compromise between not being overly alarmist and not warning too late for necessary action to be initiated. It is a probability figure that individuals and governments can comprehend. An alert such as this demonstrates that the IAWN is functioning. Further, it ensures the flow of communications from IAWN to the public and the United Nations.

## Slide 11
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
11
IAWN Notification: Key Points
Impact Probability | 1.6% as calculated by NASA JPL CNEOS and ESA NEOCC
Impact Date | 24 April 2041
Impact Risk Corridor | Across Eastern Europe, the Mediterranean Sea, and Africa from the Barents Sea to the Cape of Good Hope, across the South Atlantic to the Antarctic coast, and to the South Pacific
Asteroid Size | Most likely in the range 90–160 m (300–520 ft) in diameter, but possibly in the range 50–280 meters (160–920 feet)
Expected Damage Level If Impact Occurs | Regional blast damage, likely extending up to 110 km from impact location, but possibly as far as 200km. Energy released most likely to be in the range 5–70 Mt, but possibly in the range 3–720 Mt
When Will New Information Be Available? | The asteroid will be observable, and information will be updated, through mid-December 2024 and then again starting in August 2025
Technical Information | https://cneos.jpl.nasa.gov/pd/cs/pdc25/

## Slide 12: Current Knowledge from Telescopic Observations
Davide Farnocchia
Center for Near-Earth Object Studies NASA Jet Propulsion Laboratory

## Slide 13: Discovery of asteroid 2024 PDC25
Discovery observations of 2008 TC3
Credit: Catalina Sky Survey
Asteroid 2024 PDC25 was discovered on June 6, 2024 by the NASA-funded Catalina Sky Survey.
Announced by the Minor Planet Center on June 7, 2024.

## Slide 14: Orbit and tracking of asteroid 2024 PDC25
2024 PDC25 is on 1.0 au × 2.3 au orbit, with an inclination of 11° and an orbit period of 2.1 years.
2024 PDC25 has been tracked by optical telescopes since discovery. It will be observable until mid-December 2024 and again starting in August 2025.
Possible impact April 24, 2041
Sun
Discovery June 5, 2024
August 1, 2024
Earth’s orbit
2024 PDC25’s orbit
Radar observations are not possible until 2041.

## Slide 15: Physical properties of asteroid 2024 PDC25
Spectral and infrared observations from the James Webb Space Telescope provide key constraints
2024 PDC25 is an S-type (stony) asteroid.
Diameter most likely between 90–160 m, but possibly in the range 50–280 m.
Impact energy most likely to be in the range 5–70 Mt, but possibly in the range 3–720 Mt.
Size based on brightness measurements alone
Size including JWST observations

## Slide 16: Potential impact of 2024 PDC25
Currently, 1.6% probability of Earth impact in April 2041
2024 PDC25 will make a close approach to Earth in April 2041, and there is a 1.6% probability of impact.
Based on the current orbit uncertainty, the position of 2024 PDC25 in 2041 can only be predicted to within ±1.7 million km (4.3 lunar distances).
Based on asteroid population estimates, objects of the size of 2024 PDC25 impact the Earth every 35,000 years or so, on average.
On the Torino Impact Hazard Scale (0 to 10), this potential impact currently has a rating of 3. Only Apophis in 2004 reached a higher level on the Torino Scale.
As the asteroid is tracked over the coming months, the position uncertainty in 2041 will shrink, and the impact probability will change.
Moon’s orbit
Earth
Positional uncertainty of 2024 PDC25 in 2041

## Slide 17: Expected evolution of asteroid impact probability
Impact probability will evolve as asteroid observations continue until mid-December 2024
7% chance that the impact probability will be >10%
Worst case
88% chance that the impact probability will be < 1%
5% chance that the impact probability will be 1% to 10%
Other possible cases of impact probability evolution

## Slide 18: Expected evolution of asteroid location knowledge
From Earth-based observations
If 2024 PDC25 is on an impact trajectory, we cannot yet predict the impact location.
We can predict the accuracy of the impact location knowledge.
Without a space mission, we won’t know the impact location to within 100 km until 2039.
A reconnaissance mission would enable us to accurately predict the impact location much earlier.
The soonest the impact probability could reach 100% is September 2025.

## Slide 19: Impact Risk Assessment
Lorien Wheeler
Asteroid Threat Assessment Project NASA Ames Research Center

## Slide 20: Asteroid Impact Hazards
Entry and Breakup
Surface Hazards
Tsunami
Airburst or Surface Impact
Blast
Thermal
Local Ground Damage
Asteroids can cause damage by exploding in the atmosphere or by impacting Earth’s surface
Potential hazards include destructive blast waves, thermal fireballs, or tsunamis
Damage depends on asteroid properties, atmospheric entry, and impact location

## Slide 21: Asteroid Impact Hazards
Entry and Breakup
Surface Hazards
Tsunami
Airburst or Surface Impact
Blast
Thermal
Local Ground Damage
Asteroids can cause damage by exploding in the atmosphere or by impacting Earth’s surface
Potential hazards include destructive blast waves, thermal fireballs, or tsunamis
Damage depends on asteroid properties, atmospheric entry, and impact location
?
?
?
?
Properties and impact location of asteroid 2024 PDC25 are uncertain, so the potential damage is highly uncertain

## Slide 22: Impact Risk Assessment
Models millions of cases to evaluate range & likelihood of potential damage, given uncertainties

## Slide 23: What are the damage risks if the asteroid 2024 PDC25 hits Earth?
August 2024: 1.6% chance of Earth impact by an asteroid 50–280 m in diameter with 3–720 Mt of energy
If Earth impact occurs, there is a ~50/50 chance of damage to populated areas
Positional uncertainty of asteroid in 2041
Moon’s orbit
Earth
none
Notes: First to transition from Davide’s briefing, I’ll show this snapshot connecting the full orbital uncertainty region to the portion impacting earth.
Emphasize that there is currently only a 1.6% chance of earth impact by an asteroid in this size that, and that we are now going to be looking at the potential damage and risk among those potential earth impacting cases.

## Slide 24: Impact Hazard Summary
August 2024: 1.6% chance of Earth impact by an asteroid 50–280 m in diameter with 3–720 Mt of energy
none
Primary hazard is a destructive blast wave from a high-energy, low-altitude airburst
Blast damage could span multiple cities or larger provinces, potentially affecting thousands to millions of people
Significant tsunami are unlikely, but the largest impacts near coasts could cause inundation damage
If Earth impact occurs, there is a ~50/50 chance of damage to populated areas
Notes: Overview of the main types of hazards and how many people could be affected

## Slide 25: Affected Population Risks
Damage probabilities if Earth impact occurs; Earth impact probability is currently 1.6%
49%
Likely no damage from impacts over ocean or Antarctic
7%
17%
9%
1%
Large damage from impacts over land
17%
Average~50K
If Earth impact occurs, chances of no damage or large damage are both likely
>1K
43%
>10K
26%
>100K
10%
>1M
1%
0
49%
Likelihood of the impact affecting at least this many people if Earth impact occurs
Impacts over land would likely affect 1K–100K people, potentially up to ~5M people
~50K people affected on average
Notes: Then we’ll look that the overall probabilities of how many people might be affected if the asteroid hits earth. Overall, chances of no population damage or large population damage are both likely, with a
~50K people affected on average if Earth impact occurs
~51% chance of damage to populated regions among Earth-impacting cases.
Impacts over land likely to affect at least 1K–100K people
Worst cases could affect up to 5M people.
Likely no population significantly affected by remote impacts over ocean or Antarctic

## Slide 26: Ground Damage Risk Swath
Regions potentially at risk to ground damage given ranges of damage sizes and locations
Cape Town
Kananga
Lisala
Al Junaynah
St. Petersburg
Bucharest
Minsk
Chernivtsi
Athens
Murmansk
Median damage sizes
Impact Corridor
Areas potentially at risk to blast damage span a ~500-km-wide swath from South Africa to the Barents Sea, crossing Africa, the Mediterranean, and Eastern Europe
Damage risk swath shows extent of regions potentially at risk to ground damage, given ranges of potential damage locations and sizes
Black border shows range of potential airburst/impact locations
Rings show median damage sizes at sample locations

## Slide 27: Potential Ground Damage Sizes & Severities
Example over Cape Town, South Africa
Damage severities could reach unsurvivable levels near the blast, extending to larger areas of structural damage, fires, and shattered windows
Damage Level Description | 
Serious | Windows shatter, some structure damage
Severe | Widespread structure damage
Critical | Residential structures collapse
Unsurvivable | Devastation, structures flattened or burned
Median (50th%) Damage
Large (95th%) Damage
Likely damage sizes could span multiple metropolitan areas or counties
Large damage sizes could span multiple provinces or states
Cape Town
~80 km (50 mi)
~12 km (7 mi)
~130 km (80 mi)
~20 km (12 mi)
~60 km (40 mi)
~40 km (25 mi)
Cape Town
Notes: Epoch 1 damage section stats:
Damage severities could reach unsurvivable levels near airburst, extending to larger areas of structural damage, fires, and shattered windows
Outer serious damage areas are most likely between ~40–110 km (~25–70 miles) in radius (median ~80 km, 50 mi)
Large damage areas could extend out over ~130 km or so (~120 miles) or more in radius
(99th% is 160 km, max modeled is 240 km)

## Slide 29
Average affected population along potential impact regions
EXERCISE EXERCISE EXERCISE
Damage probabilities if Earth impact occurs
Possible asteroid sizes (m)
50
280
Most likely size: 90–160
Rocky composition
Today is 1 August 2024.
1.6% probability of Earth impact in ~17 years
Potential impact
24 April 2041

## Slide 30
EXERCISE EXERCISE EXERCISE
IAWN notification
1 August 2024
It is now October 2024.
16.5 years until potential impact
Potential impact
24 April 2041

## Slide 31
EXERCISE EXERCISE EXERCISE
IAWN notification
1 August 2024
It is now October 2024.
16.5 years until potential impact
Potential impact
24 April 2041

## Slide 32
29 October 2024
SMPAG shares recommendations
August 2024
IAWN issues notification about potential impactor
10 & 11 October 2024
SMPAG meets in Milan, Italy
August to October 2024
Delegates of the UN-endorsed Space Mission Planning Advisory Group (SMPAG) meet virtually on a recurring basis to assess space mission options
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
The impact probability is now 18%. There is an 82% chance the probability of Earth impact will be >1% when observations end in December.

## Slide 33
Recommendations for Space Mission Options
Detlef Koschny
Chair, Space Mission Planning Advisory Group
(SMPAG)
9th IAA Planetary Defense Conference
Scenario date: 29 October 2024

## Slide 34: Space Mission Planning Advisory Group
AEM (Mexico)
ASI (Italy)
BELSPO (Belgium)
Czech Republic
CNSA (China)
CNES (France)
CSA (Canada)
DLR (Germany)
ESA
FFG (Austria)
JAXA (Japan)
ISA (Israel)
KASI (Korea)
NASA (USA)
ROSA (Romania)
ROSCOSMOS (Russia)
SSAU (Ukraine)
SUPARCO (Pakistan)
UK Space Agency (UK)
SMPAG members as of January 2024
+ Observer or
ex-officio status:
ASE, COSPAR, ESO, IAA, IAU, IAWN, SWF, UNOOSA
Endorsed by the UN Committee on the Peaceful Uses of Outer Space in 2013

## Slide 35: Excerpts from Terms of Reference
“The purpose of the SMPAG is to prepare for an international response to a NEO impact threat through the exchange of information, development of options for collaborative research and mission opportunities, and NEO threat mitigation planning activities.”
Reference: SMPAG Terms of Reference, https://www.cosmos.esa.int/web/smpag/terms_of_reference_v2

## Slide 36
Overview for NEO Threat Response
EXERCISE EXERCISE EXERCISE
EXERCISE EXERCISE EXERCISE
36
> 1 %
< 50 years
> 50 m

## Slide 37
MISSION OPTIONS TIMELINE

## Slide 38: Five SMPAG Recommendations
1 |  | Start, as soon as possible, the initial design phases (phases A/B) of a fast flyby reconnaissance mission.
2 |  | Consider re-tasking an already flying spacecraft to perform an early reconnaissance of the target asteroid.
3 |  | Start, as soon as possible, the initial design phases (phases A/B) of a solar electric propulsion (SEP) rendezvous reconnaissance mission, independently of the implementation of a flyby reconnaissance mission.
4 |  | Start, as soon as possible, the initial design phases (phases A/B) of in-space mitigation missions, based on the following concepts, including the risk assessment on each option: kinetic impactor (KI) and ion beam deflection (IBD).
5 |  | Perform detailed simulations assessing the possibility to disrupt an asteroid by an impulse transfer. The work should be done by several SMPAG delegations independently.

## Slide 40
Avg. affected population along potential impact regions
EXERCISE EXERCISE EXERCISE
SMPAG Recommendations
Possible asteroid sizes (m)
50
280
Most likely size: 90–160
Rocky composition
Potential impact
24 April 2041
It is October 2024
16.5 years until potential impact; 18% chance of impact
Affected people among Earth-impacting scenarios
>1K
43%
>10K
26%
>100K
10%
>1M
1%
0
49%
Flyby Recon
Retask for Recon
Rendezvous Recon
In-Space Mitigation
Disruption Modeling

## Slide 41
Participant Discussion
What did you learn during the panel?
What in the panelists’ comments aligned with your expectations? What surprised you?
Did your perspective on planetary defense change in any way after listening to the panelists? If so, how?
What are the implications of the panelists’ comments for your own work?
What concrete actions could be taken to make progress on the issues raised by the panelists?
If you could ask the panelists to elaborate on one specific point, what would it be?

## Slide 42
Share Your Perspectives
Which recommendation about asteroid reconnaissance would you advocate that your government prioritize, given the current level of risk?
  Fast flyby reconnaissance mission
  Re-tasking already flying spacecraft for reconnaissance
  Rendezvous reconnaissance mission
Which recommendation related to Earth impact prevention would you advocate that your government prioritize, given the current level of risk?
  Initial design phases of in-space mitigation missions
  Detailed simulations assessing the possibility of asteroid disruption