## Slide 1: Options and Uncertainties for Nuclear Mitigation in the 2025 Hypothetical Asteroid Threat Exercise Scenario
Catherine S. Plesko, Stephen A. Becker, Mark B. Boslough, Wendy K. Caldwell, Megan L. Harwell
May 2025
LA-UR-25-24025

## Slide 2
The Delta V Criteria: Shifting Technical Risk
The velocity threshold criteria were intended to be simple and conservative:
  For a uniform impulse from ablation of the burst-facing surface:
    If delta v < 0.1 vesc, the object is very unlikely to disrupt.
    If delta v > 10 vesc, the object is very likely to strongly disrupt.
A lot of previous work has assumed a high-speed trajectory, not rendezvous
  Limited control of height of burst
  Proximal operations have a high-risk of premature impact
The hypothetical threat object size range and orbit make it difficult to adhere to the delta V heuristics for stand-off bursts
  Up to a dozen impulses required in some cases
This scenario allows rendezvous, which make proximal operations viable
  Surface bursts couple much more energy to the target
  Energy deposition is highly localized

## Slide 3
Hypothesis: A Single 1 MT Burst in Close Proximity Could Strongly Disrupt the Hypothetical Threat Object.
Top: Romanian Palace of Parliament, courtesy Wikipedia
Bottom: : Landsat image of Eniwetok Atoll, showing some of the craters Glasstone and Dolan’s model was derived from. (NASA/USGS)
2024 PDC is of comparable size, mass to the PDC 2011 conference venue, if substantially weaker.
A 1 MT surface burst on Earth makes a transient crater of a size comparable to the threat object.
  300-500 m diameter
  50-100 m depth
  Glasstone and Dolan, pp. 253-257
A 1 MT surface burst on the threat object is not expected to make a smaller crater.
  lower surface gravity, no air,
  expected to be weaker than the rock under load used above.
Koa crater on Eniwetok Atoll is a potential near neighbor

## Slide 4
The Koa Crater in the Eniwetok Atoll is a Potential Near Neighbor
Top: Landsat image of Eniwetok Atoll, showing the Mike and Koa craters. (NASA/USGS)
Bottom: Frontispiece, UCRL-12172
Described in “Nuclear Cratering Experience at the Pacific Proving Grounds” (UCRL-12172)
  Yield = 1.3 MT
  Final crater diameter: 1.1 km
  Transient crater diameter 400-500 m
  Excavation depth: 41 m
Extensive studies of the crater were done by the USGS PEACE Program in the 1980’s. (USGS Open-File Report 86-419 & etc. )

## Slide 5
The Amount of Material Displaced in a Strong Disruption Should be Predicted to be at Least that of a Similarly Sized Transient Crater.
Image by B. French and D. Kring, LPI
The transient crater is that which exists at the end of the excavation stage on Earth.
  Third frame from the bottom
  It is deeper and narrower than the final crater.
  Over geologic time on Earth, the transient crater slumps, becoming wider and shallower.
The modification process does not apply to our scenario, so we use the transient crater, not the final crater.
We propose these dimensions as a lower bound.
We hypothesize that if the device is big enough to move at least that much material on Earth, it should do so in space.

## Slide 6
Glasstone and Dolan Scaled Crater Predictions Suggest Disruption of 2024 PDC by a Near-Surface Burst is Possible.
Right: Glasstone and Dolan (1977) p. 255, Fig. 6.72 a
Transient crater dimensions for Y = 1 kt are experimentally determined
  Dimensions can be scaled to other yields
  d(Y) = d(1kt)*Y^1/3
  Scaled predictions validated against experiments
Cube root scaling example:
  Scaled DOB = DOB/Y^1/3 = 0/1000^1/3 = 0
  30 m < D(1kt, HOB=0) < 50 m
  300 < D(1kt)*1000^1/3 < 500 m
Predicted transient crater D > D threat object
  lower surface gravity,
  target expected to be weaker
Notes: Note- even for 10-100kt, crater diameter is ~ threat object size.
FIXME ADD CRATER GRAPHIC

## Slide 7
A community standard definition may be beneficial
Mitigation Outcome Requirements Used in This Work
The initial target parameters should over-predict the difficulty of disruption
No remaining fragment should be larger than Tunguska
  We use d = 30 m, the lower end of Tunguska diameter predictions
Q*m vs Q*D
  Energy required to mitigate to our preferred specifications
  Energy required to disrupt so that the largest fragment is 50% of initial
Fragments should be left with sufficient velocity to miss Earth
  Not well-posed
  Solar wind effects on smaller particles
  What amount of disrupted mass at what size distribution is tolerable?

## Slide 8
Cautious Simplification Through a Steel Man Argument
Right: A steel man argument envisioned as a graphic novel character. Image generated by the author using DALL-E by OpenAI on 4.3.2025
A rhetorical technique to address the strongest form of an argument.
We believe 2024 PDC to be structurally weaker than solid SAE 304 stainless steel.
We can model 2024 PDC as solid steel, which has well-known constitutive properties.
If a steel target disrupts, we believe the attempt would likely also disrupt 2024 PDC.

## Slide 9
Steel vs. S-type Asteroid: 2-3 Orders of Magnitude Stronger
Right: A steel man argument envisioned as a graphic novel character. Image generated by the author using DALL-E by OpenAI on 4.21.2025
 | Yield | Tensile | Shear
S-type | 0.2-5 MPa | < 10 MPa | < 10 MPa
SAE 304 | 294 MPa | 200 Mpa | 370 MPa
We don’t know the internal properties of 2024 PDC, or most asteroids, very well.
The disruption threshold is dependent on these properties
Specific cases that involve gravity regime cratering may be less sensitive to target strength
  These cases involve high energies
Notes: Tensile and shear values for Tuff, Yield taken from ATAP aerodynamic strength predictions

## Slide 10
The Pagosa Hydrocode
Pagosa is a 1-3D Eulerian finite difference code
Fixed mesh (non-AMR)
Used to study high-velocity impacts and high explosives phenomena.
Weseloh et al. (2010)
Verification and validation for crater modeling by Heberling et al. (2017)
Was tested in the Stickle et al. (2019) code benchmarking study prior to DART.
Notes: The second multi-physics code that we use is PAGOSA,
an Eulerian finite difference hydrocode.
PAGOSA uses different numerical methods than FLAG,
And was originally developed by Wayne Weseloh and co-authors
to study high-velocity impacts and high explosives experiments.
PAGOSA was validated for modeling hypervelocity impacts into geologic materials
by Tamra Heberling in 2017,
and again for the DART code benchmarking study in 2019.

## Slide 11
2024 PDC Epoch 2 Steel Man Model Input
Pagosa model at t=0
Pagosa:
  Hydrodynamics only, no x-rays.
  dx = 50 cm fixed mesh
  2d-axisymmetric
Energy pill has variable internal energy sourced into a copper sphere:
  d = 2 m, Mie-Gruenisen Copper EOS
  1 ton TNT < Y < 500 kt TNT
  At the surface along the long axis, partially buried
Threat object
  95th percentile ellipsoid (121m x 124 m x 236 m)
  Homogeneous Sesame EOS 4272
  Preston-Tonks-Wallace strength
    Yield stress: 0.002944 Mbar
  Johnson-Cook damage
    spall stress: 0.05861 Mbar

## Slide 12
2024 PDC Epoch 2 Steel Man Model Results
Yield (kt) | Disrupted ? | Q*D Achieved? | dV > 100 cm/s ? | Energy Imparted
500 | Yes, t < 0.4 s | Yes, t < 0.2 s | Yes, t < 0.1 s | 170 kt deposited, ~50 kt does work on solids
200 | TBD | TBD | TBD | 60 kt deposited, ~ 30 kt does work on solids
100 | TBD | TBD | TBD | 30 kt
10 | No | No | No | 3.7 kt
1 | No | No | No | 0.55 kt
0.001 | No | No | No | ~10 lbs TNT

## Slide 13
2024 PDC Epoch 2 Steel Man Model Results: Non-Disruption Cases
Yield (kt) | First shock crossing | Time shock attenuated to -pfail < P < yld str., -0.05861 < P < 0.002 Mbar | Damage at time of attenuation
10 | t = 0.0383 s | t > 0.07 s | TBD
1 | t = 0.0387 s | t = 0.0676 | minimal
0.001 | t = 0.0412 s | t = 0.0412 | minimal
Notes: 1 kt case shown, colored by damage

## Slide 14
2024 PDC Epoch 2 Steel Man Model Results
Contiguous portions of the steel target subject to the 500 kt blast with damage < 1 are meter-scale or smaller at late time.
A single 500 kt – 1 Mt contact burst appears sufficient to strongly disrupt a steel object of the same volume as the 95th percentile case of 2024 PDC.
It should be sufficient to disrupt any instantiation of 2024 PDC.
Parameter studies are ongoing to constrain a lower bound estimate of the energy required to mitigate, for completeness, does not drive mission design.

## Slide 15
2024 PDC Epoch 2 Geologic Model Input
Pagosa:
  Hydrodynamics only, no x-rays.
  dx = 50 cm fixed mesh
  2d-axisymmetric
Energy pill is 500 kt internal energy sourced into a copper sphere
  d = 2 m
  Mie-Gruenisen EOS
  At the surface along the long axis, partially buried
Threat object
  95th percentile case
  SESAME Nevada Alluvium EOS
    Porosity implicit in the EOS to include PdV work.
  Kospall strength model, cohesion ~ yield strength.
  Homogeneous material.
Right: The 2024 PDC hypothetical threat object envisioned as a graphic novel character, contemplating a Steel Man action figure. Image generated by the author using DALL-E by OpenAI on 4.21.2025

## Slide 16
2024 PDC Epoch 2 Geologic Model Results
Right: Hydrodynamics simulation of a 500 kt energy pill tangent to the 95th percentile threat object.
As expected from the steel man models, all cases strongly disrupt.
95th percentile case model suggests strong disruption by t = 1.0 s
  One Tunguska-sized contiguous piece
Craters made by explosions this size are in the gravity regime.
  May be less sensitive to details of target strength.

## Slide 17
Potential Applications
Right: A cross-section of a shock wave traveling through a disrupting steel target. Pagosa 500 kt steel simulation at t=0.01 sec.
Disruptions are insensitive to:
  B-plane direction
  perihelion timing
As a main option:
  2032-2039, per Barbee et al. (this meeting)
Reserve options (upon main option failure)
  Post Northward IBD: 2034-2039
  Post Southward IBD: 2035-2039
  Post Southward Partial IBD: 2035-2039
  Post KI Backup Dates: 2037-2039

## Slide 18
Remaining Questions
Right: A cross-section of a disrupting steel target, colored by damage, thresholded to D< 1. Pagosa 500 kt steel simulation.
Mission options for contact binaries
  2+ devices placed carefully?
Time required for dispersal of decameter scale fragments
A specific consensus definition of mitigation outcome requirements
  based on expected ground effects?