## Slide 1
The post-DART heliocentric orbit of Didymos and implications for the effectiveness of the DART impact
Steven R. Chesley, Rahil Makadia, David Herald, Davide Farnocchia, Shantanu P. Naidu, Alexandros Siakas, Damya Souami, Paolo Tanga, Sotirios Tsavdaridis, and Kleomenis Tsiganis
Li et al. 2023

## Slide 2: DART and Didymos
The backstory
NASA’s DART spacecraft impacted Dimorphos, the satellite of the Didymos system in Sept. 2022
A key objective was to measure the effects of the impact and the efficiency of the deflection
The efficiency is quantified by the momentum enhancement factor But some care is needed since ejecta and spacecraft momentum vectors may not be aligned. (Statler et al. 2022)

## Slide 3: Previous β results from DART
Based on change in Dimorphos orbit
DART caused the ~12h orbital period of Dimorphos to drop by ~33 minutes (Naidu et al. 2024)
  Traceable to transverse deflection of Dimorphos (Naidu et al. 2024) ∆VT = 2.63 ± 0.06 mm/s
  This result relied on a huge number of telescope observations (~38,500 images from 28 telescopes, Moskovitz et al. 2024)
This ∆V implied βDimo ≈ 2.2 – 4.9, assuming a range of Dimorphos densities (1.5–3.3 g/cm3) (Cheng et al. 2023)
  For an assumed density of 2.4 g/cm3 :
Cheng et al. 2023

## Slide 4: The heliocentric deflection
An alternate approach to measuring β
Predicted to be measurable by 2024 (Makadia et al. 2024)
But the heliocentric is tiny
  For equal density binary components, ~115× smaller than Dimorphos deflection, so perhaps ~20 𝜇m/s
Relies on a range of precise observational data types
  Ground-based RA-Dec
    ~5900 observations, 1996-2025
  DART OpNavs
    3 used in fits
  Radar delay
    5 in 2003, 4 in 2022 (post-impact)
  Stellar occultations
    22 successful campaigns from Oct. 2022-Mar. 2025
    These were they crucial measurements for this work

## Slide 5: Didymos Occultations
A. Asai
E. Barbotin
J. Broughton
N. Carlson
A. Cazaux
S. Cikota
K. Cobble
F. Colas
J. Dauvergne
R. Dunford
D. Dunham
J. Dunham
J. Flores
D. Gault
K. Getrost
K. Guhl
J. Hanus
T. Hayamizu
D. Herald
K. Hosoi
M. Ida
R. Jones
K. Kitazaki
G. Langin
A. Leroy
B. Lott
G. Lyzenga
P. Maley
N. Manago
A. Manna
J. Moore
Y. Nakamura
T. Nemoto
H. Noda
R. Nolthenius
S. Preston
L. Rousselot
M. Sanchez
M. Skrutskie
S. Sposetti
M. Takimoto
R. Trank
R. Venable
H. Watanabe
F. Weber
B. Whitehurst
H. Yamamura
M. Yamashita
H. Yoshihara
22 total occultations (including 2 rejected outliers)
Around ⅓ are sub-milliarcsecond precision
Most precise is 0.1 mas(!)
Contributing Observers
Figure of Didymos

## Slide 6: Estimate
First, apply a priori constraint from independent sources
DART momentum:
  Cheng et al. 2023
Didymos system mass:
  Naidu et al. 2024
Ejecta direction:
  Hirabayashi et al. 2025
Everything except β⊙ is reasonably well known
  Assume 1 < β⊙ < 5
β⊙≈3
β⊙≈1
β⊙≈2
β⊙≈4
β⊙≈5

## Slide 7: Estimate
Next, estimate the orbit and (& Yarkovsky effect)
is well defined in all components
Yarkovsky signal has SNR~20 and is well-separated from
β⊙≈3
β⊙≈1
β⊙≈2
β⊙≈4
β⊙≈5

## Slide 8: We can now calculate β
We start by projecting in the heliocentric along-track direction ()
Use the value of to compute the heliocentric along-track momentum enhancement parameter,

## Slide 9: Why is β so much lower?
Because Dimorphos has (relatively) low bulk density
But we need to “connect” Dimorphos β and heliocentric β
  Because the heliocentric ejecta momentum is different than that of the mutual orbit
  We suppose that 0-10% of the Dimorphos ejecta is trapped in the Didymos system
With that, we can compute the bulk density of the components
  = 1540 ± 220 kg/m3
  = 2600 ± 140 kg/m3

## Slide 10: Concluding remarks
We find β ≈ 2 for the DART impact
  Ejecta contributed about half of the total momentum exchange
Dimorphos under-dense relative to Didymos
  Density ratio
  Important constraint on formation processes?
Hera will provide mass & density for Dimorphos
  This will afford an independent estimate of