## Slide 1: Spheral Simulations of the Atmospheric Entry and Energy Deposition of PDC25 Threat Scenario Asteroids
Evan Bjonnes
Jason M. Pearl, Kathryn M. Kumamoto, J. Mike Owen
May 5-9, 2025
IAA Planetary Defense Conference 2025
Stellenbosch, Cape Town, South Africa

## Slide 2: Overview
Atmospheric airbursts can have dire consequences for Earth, from the generated shockwave in the air and from any meteoritic material that strikes the surface
Several factors affect how an incoming asteroid will interact with Earth’s surface and atmosphere:
  Incoming angle
  Asteroid size
  Asteroid material properties
    Coherent rock vs rubble pile asteroid
    Porosity
    Degree of metal content
2013 Chelyabinsk Airburst, from Wikipedia.org

## Slide 3: Bolide Parameter Model Space
2025 PDC Hypothetical Asteroid Impact Scenario Epoch 1 Parameters
Physical Property | 5th Percentile | 50th Percentile | 95th Percentile | 100th Percentile
Diameter (m) | 77.09 | 127.05 | 191.17 | 277.84
Bulk Density (g/cm3) | 1.886 | 2.062 | 2.417 | 2.794
Porosity | 0.443 | 0.4 | 0.245 | 0.2
Mass (kg) | 4.5246E+08 | 2.2142E+09 | 8.8424E+09 | 3.1376E+10
Surface Escape Velocity (cm/s) | 3.958 | 6.821 | 11.112 | 17.364
Absolute Magnitude | 22.398 | 21.773 | 21.345 | 21.438
Albedo | 0.326 | 0.214 | 0.14 | 0.061
Taxonomic Type | S | S | S | S

## Slide 4: Spheral Model Setup
We use Spheral++, our Lagrangian smooth particle hydrodynamic code with Fluid-Solid Interface SPH (FSISPH) implementation
Model space is set up with designated bolide properties (size, density, strength, etc) and surrounding air particles
As time progresses, Spheral advances air to the right, simulating bolide motion to the left
Incoming air properties (temp, density) calculated according to prescribed atmospheric conditions and entry angle
From Pearl et al, 2023
Bolide
Initialized Air
“Incoming” Air
Model Space

## Slide 5: Example Model – 127m Diam, 20° Entry
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600
Midsize,
Longest Traverse

## Slide 6: Example Model – 127m Diam, 20° Entry
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600
Midsize,
Longest Traverse

## Slide 7: Example Model – 127m Diam, 20° Entry
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600
Midsize,
Longest Traverse

## Slide 8: Example Model – 127m Diam, 20° Entry
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600
Midsize,
Longest Traverse

## Slide 9: Example Model – 127m Diam, 20° Entry
Midsize,
Longest Traverse
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600

## Slide 10: Example Model – 127m Diam, 20° Entry
Midsize,
Longest Traverse
-500
500
0
Distance (m)
1000
-1000
Distance (m)
-200
600
We performed this analysis for the 4 asteroid sizes and corresponding densities, both with and without material strength, for the three incoming angles.

## Slide 11: For a Given Entry Angle, Energy Deposition Height Corresponds with Bolide Size
Bolide With Strength
Bolide Without Strength
20° Entry
(tree not to scale)

## Slide 12: Strength Plays a Pivotal Role in Bolide Evolution
Only one case using a hydrodynamic bolides makes it to the ground “intact” (and that is debatable)
Distance (m)
1000
1000
0
Elevation (m)
-400
1000
Ground
Distance (m)
1000
1000
0
Elevation (m)
-200
800
Ground
Most Fully Hydro Bolides
90° Incoming Angle, 278 m Diameter - Hydro

## Slide 13: Strength Plays a Pivotal Role in Bolide Evolution
Only one case using a hydrodynamic bolides makes it to the ground “intact” (and that is debatable)

## Slide 14: Strength Plays a Pivotal Role in Bolide Evolution
Only one case using a hydrodynamic bolides makes it to the ground “intact” (and that is debatable)

## Slide 15: Strength Plays a Pivotal Role in Bolide Evolution
Only one case using a hydrodynamic bolides makes it to the ground “intact” (and that is debatable)

## Slide 16: Strength Plays a Pivotal Role in Bolide Evolution
In bolides with strength, all models have portions of intact material reach the surface

## Slide 17: Strength Plays a Pivotal Role in Bolide Evolution
In bolides with strength, all models have portions of intact material reach the surface

## Slide 18: Strength Plays a Pivotal Role in Bolide Evolution
In bolides with strength, all models have portions of intact material reach the surface

## Slide 19: Strength Plays a Pivotal Role in Bolide Evolution
In bolides with strength, all models have portions of intact material reach the surface
~250 – 850 m separation

## Slide 20: Strength Plays a Pivotal Role in Bolide Evolution
In bolides with strength, all models have portions of intact material reach the surface
90° Entry
45° Entry
20° Entry

## Slide 21: Initial Impressions
Material strength plays a huge role in affecting the fate of an incoming asteroid
Asteroids incoming on shallower trajectories have longer transits through the atmosphere and are more likely to become fireballs
Ongoing Work:
  Verifying these results with 3D simulations
  Using energy deposition curves as inputs for blast wave modeling

## Slide 22
Thank you for your attention!