## Slide 1: Developing a Robust Flyby Reconnaissance Capability for Planetary Defense
Nancy L. Chabot, Justin A. Atchison, Rylie Bull, Andrew S. Rivkin, R. Terik Daly, Ronald-L. Ballouz, Olivier S. Barnouin, Andrew F. Cheng, Carolyn M. Ernst, Angela M. Stickle, Evan J. Smith, Joseph J. Linden, Benjamin F. Villac, Jodi R. Berdis, Dawn M. Graninger, Sarah Hefter
Johns Hopkins University Applied Physics Laboratory

## Slide 2
In 2021, the United States adopted protocols that recommended executing a spacecraft reconnaissance mission in any scenario that meets the SMPAG criteria and also has sufficient time to conduct the mission prior to the predicted impact.
“Such a mission can provide information critical to determining whether prevention is necessary and, if so, to enabling its success.”
SMPAG criteria:1. Earth impact is predicted to be within 50 years. 2. Impact probability is assessed to be >1%. 3. Object is determined to be >50 m in size (or H <26 if only brightness data are available).

## Slide 3: Developing a spacecraft reconnaissance capability for the most likely impact threat is a necessity
50-m is the smallest to warrant a mission
Earth impact roughly every ~1,000 years
Only ~10% of these NEOs have been found
50-m objects are the smallest NEOs recommended for a space mission under current SMPAG (2017) and U.S. protocols (2021).
50-m objects impact the Earth much more frequently than larger objects, so they are the NEOs most likely to trigger a space-based mission.
Even with NEO Surveyor and Rubin Observatory, ~half of the 50-m NEOs will be left undiscovered. Thus, warning times may be short.

## Slide 4
Developing a spacecraft reconnaissance capability for the most likely impact threat is a necessity and a U.S. priority
Recommendation: The next planetary defense demonstration mission should be a rapid-response, flyby reconnaissance mission targeted to a challenging (~50-100-m) NEO
Goal: Develop Technologies for NEO Reconnaissance, Deflection, and Disruption Missions
Short Term Actions: Collaborate on technologies for rapid response, reconnaissance, and characterization of in-space objects. Create plans for the development, testing, and implementation of NEO reconnaissance mission systems.

## Slide 5: Enable a reconnaissance of >90% of the potential asteroid threat population
The darkest timeline
You don’t pick the asteroid – the asteroid picks you.
Synthetic Threat Population:
2340 potentially hazardous asteroids (PHA) achieve their minimum Earth distance in the 2030s
1

## Slide 6: Enable a reconnaissance of >90% of the potential asteroid threat population
You don’t pick the asteroid – the asteroid picks you.
1
Ballistic spacecraft trajectories were computed for the synthetic threat population, resulting in millions of possible trajectories.
Max time of flight | 2.5 yrs
Min solar dist. | 0.9 AU
Max solar dist. | 2.0 AU
Max approach solar phase angle | 90 deg
Max flyby speed | 25 km/s
Max launch C3 | 30 km2/s2
Flyby conditions that encompass >90%
Notes: Demonstrating this capability for the most challenging conditions shows that it can be applied to ≥90% of the potential asteroid threat population

## Slide 7: Demonstrate flyby reconnaissance for a ~50-m NEO
You don’t pick the asteroid – the asteroid picks you.
2
The demonstration must test the limits of the performance in a stressing flyby case.
Max time of flight | 2.5 yrs
Min solar dist. | 0.9 AU
Max solar dist. | 2.0 AU
Max approach solar phase angle | 90 deg
Max flyby speed | 25 km/s
Max launch C3 | 30 km2/s2
Flyby conditions that encompass >90%
Most flyby encounters won’t be of a half-lit 50-m object at 25 km/s – but if the reconnaissance capability can handle that stressing case, it can be deployed for >90% of the potential asteroid threat population.
Notes: The demonstrated capability could then also be applied to the less challenging case of a larger object, should such a need arise in the future.

## Slide 8: Obtain the information needed to determine if and where the object would impact the Earth
3
Example from Planetary Defense Conference Exercise – 2019
https://cneos.jpl.nasa.gov/pd/cs/pdc19/
Uncertainty
region
EXERCISE ONLY!
After a flyby, the impact location is known to within ~100 km
EXERCISE ONLY!
With telescopes only, the impact uncertainty region can span the globe
Notes: Left side– Day 2 of exercise – July 2019 is date
Right side – Day 3 of exercise – Dec 30, 2021 – flyby just happened

## Slide 9: Determine key properties of the asteroid to inform decision makers
4
Determine the asteroid’s size
Determine if the asteroid is mostly rocky or metallic
Determine if there is a single object or multiple objects of concern
Determine the asteroid’s surface characteristics
vs
DART image
of Dimorphos
?
Ordinary chondrite NWA 869
By H. Raab (User:Vesta) - Own work, CC BY-SA 3.0
NASA/Johns Hopkins APL
Cape York iron meteorite
Photo courtesy of Chuck Sutherland

## Slide 10: Determine key properties of the asteroid to inform decision makers
4
Determine the asteroid’s size
Asteroid size knowledge
https://cneos.jpl.nasa.gov/pd/cs/

## Slide 11: Determine key properties of the asteroid to inform decision makers
4
Determine the asteroid’s size
Flyby imaging greatly reduces the uncertainty in the NEO’s size
Asteroid size knowledge
= ±20 m
https://cneos.jpl.nasa.gov/pd/cs/

## Slide 12: Determine key properties of the asteroid to inform decision makers
4
Determine if the asteroid is mostly rocky or metallic
vs
Ordinary chondrite NWA 869
By H. Raab (User:Vesta) - Own work, CC BY-SA 3.0
Cape York iron meteorite
Photo courtesy of Chuck Sutherland
Without a direct mass measurement, uncertainty in whether the object is rocky or metallic creates large uncertainty in the potential damage
From Planetary Defense Tabletop Exercise 4 (2022) – Illustrating the range of potential damage due to uncertainties in the asteroid’s properties.
EXERCISE ONLY!
~3–4 g/cm3
~7–8 g/cm3

## Slide 13: Determine key properties of the asteroid to inform decision makers
4
Determine if the asteroid is mostly rocky or metallic
vs
Ordinary chondrite NWA 869
By H. Raab (User:Vesta) - Own work, CC BY-SA 3.0
Flyby measurements can distinguish between mostly rocky vs metal-dominated NEOs
Iron powders
<150 µm
<45 µm
(Bramble et al., 2021)
Bennu (Hamilton et al., 2021)
Other spectra from RELAB Database
Chelyabinsk (OC)
Norton County (aubrite)
Murchison (CC)
ALH 81001 (eucrite)
EET 90102 (EC)
Determine if the asteroid is mostly rocky or metallic
vs
Ordinary chondrite NWA 869
By H. Raab (User:Vesta) - Own work, CC BY-SA 3.0
Cape York iron meteorite
Photo courtesy of Chuck Sutherland
~3–4 g/cm3
~7–8 g/cm3
Thermal IR Spectral Measurements

## Slide 14: Determine key properties of the asteroid to inform decision makers
4
Determine if there is a single object or multiple objects of concern
?
Flyby imaging can determine the number of objects of concern
Lucy L’LORRI image
Selam (220 m each)
Dinkinesh (790 m)
NASA/Goddard/SwRI/Johns Hopkins APL

## Slide 15: Determine key properties of the asteroid to inform decision makers
4
Determine the asteroid’s surface characteristics
DART image
of Dimorphos
NASA/Johns Hopkins APL
Flyby imaging of ≤0.5 m/pixel can reveal surface features on the scale needed to inform potential mitigation options
DART approach images of Dimorphos, cropped to 50-m diameter
2 m/pixel
1 m/pixel
0.5 m/pixel

## Slide 16: You don’t pick the asteroid – the asteroid picks you.
Enable a flyby of >90% of the potential asteroid threat population
Demonstrate flyby reconnaissance for a ~50-m NEO
A technology demonstration mission is necessary to develop this robust reconnaissance capability and advance planetary defense preparedness.
1
2
3
4
Obtain the information needed to determine if and where it would impact the Earth
Determine key properties of the asteroid to inform decision makers