## Slide 1
Arash Safaei, Matteo D.L. Dalla Vedova, and Paolo Maggiore
Department of Mechanics and Aerospace Engineering (DIMEAS), Politecnico di Torino, Italy
“Harnessing the Sun for the Moon: Thermo-Optical Analysis and Orbital Simulation of a Lunar Solar Power Satellite for Future Lunar Exploration”

## Slide 2
Presentation Outline
State of the Art
Model Design
Simulations
Results
Conclusion
Dyson Sphere combined with the most promising SBSP Satellite
Development of a 3D model based on the SPS Type 3 satellite.
Optical, Thermal and Orbital Simulations with Ansys, Matlab and STK
Outputs of the implemented model and simulations
Comparison with existing terrestrial facilities

## Slide 3
State of the Art
Continuous Energy Generation (1367 [W/m²])
High Energy Efficiency
Scalability
Minimal Environmental Impact
Flexible Energy Distribution
Space-Based Solar Power Satellite
Dyson Sphere
and
can be combined
together to provide both Earth and the Moon the energy needed to satisfy global power demand.
Our actual Type Level:

## Slide 4
Implemented Design: SPS Type 3
Minimized Launch Costs
Minimized Solar Panel Surface
High Modularity & Scalability
High Energy Collection Capability
Alignment with Current Technological Advances
Less complex to Implement and Simulate
NASA Report available
Why this configuration?
100 MW Satellite
2 GW Satellite
from
to

## Slide 5
SUBSYSTEMS:
In target orbit, PV cells capture sunlight and convert it into energy
3D CAD Model
Model Setup
The energy is sent to the Moon in the form of microwave or laser beam.
A ground receiver captures the beam and converts it into electricity.
The electricity is then sent to the power grid.
MIRROR
ABSORBER
ANTENNA
RECTENNA

## Slide 6
where:
n = number of Satellites
Scalability
Modularity
...
Final Delivered Power:
Matematical Model
Mirror’s surface
Capacity Factor of the Ground Station
Efficiency of component i
Bottleneck
Thermal Dynamics

## Slide 7
Experimental work performed in Polimi Propulsion Lab:
Pulsed CO2 Laser Beam hitting a sensitive disc (brass)
Model Validation
The Mirror and the Absorber surface can be modeled in the same way!

## Slide 8
Optical Simulation
ANSYS SPEOS
Since it is not possible to recreate the 1:1 scale model on Ansys due to graphical and computational limitations, the model was scaled down to 1:130000.
The model used to simulate optically satellite configuration consists of:
Radiative plate (Sun Radiation)
3 Radiative Sensors (Output)
2 Parabolic Mirrors (Hexagons)
2 PV’s Absorbers (Elliptical)
1 Transmitting Antenna (Beaming)

## Slide 9
Optical Simulation
ANSYS SPEOS OUTPUT:
9 m
P = 50 MW
°
Absorber

## Slide 10
Heat Flux: 1367 [W/m²]
Final T: 59.3 [°C]
Primary Creep T: ~198 [°C]
Thermal Simulation
Material: Aluminum
The aim of the Thermal Simulation is to estimate the transient and final T [°C] values of the mirror and absorber, ensuring they remain below the material's creep temperature.
This limitation guarantees the preservation of mechanical properties during the operational phase, extending mission's duration.
ANSYS THERMAL TRANSIENT: Mirror
Thickness: 0.75 [micron]
Mass: 115 [kg]
Equilibrium Time: ~2000 [s]

## Slide 11
Heat Flux: 900,000 [W/m²]
Final T: 1402 [°C]
Primary Creep T: ~1440 [°C]
Thermal Simulation
Material: Graphite
Thickness: 0.75 [mm]
Mass: 40 [kg]
The aim of the Thermal Simulation is to estimate the transient and final T [°C] values of the mirror and absorber, ensuring they remain below the material's creep temperature.
The thickness of both the absorber and mirror is set equal to the sensitive disc tested in lab at Polimi.
ANSYS THERMAL TRANSIENT: Absorber
Equilibrium Time: ~0.5 [s]

## Slide 12
Ansys Time: ~2 h
Simulator Time: 86 s
Implemented Model VS Ansys Simulations
The results of the simulations performed with Ansys are used to cross-check the implemented model output.
The proposed model is then augmented with the results of the dedicated simulations, leading to more robust and accurate Simulator.
MODEL VALIDATION
Just to mesh the Mirror!
To size the entire System
0.093%
Error between Ansys and Model?
Absorber Heating Profile

## Slide 13
HOW MANY GROUND STATIONS?
It depends upon the max allowable heat flux on ground (~200 W/m² for RF of 2.45 GHz)
Orbital Simulation
Earth 18.7 [TW] 9360
N° of Satellites
Objective of the orbital simulations? To determine:
N° of Rectennas
Orbital and Ground Configuration
INPUT DATA:
USA 1.1 [TW] 550
Torino 550 [MW] 0.28
Power Consumption
N° of Satellites
Orbit Type: LLO
Coverage: 100%
N° Satellites: 3
2 GW Satellite
Moon ??? [MW] ?
Power: 100 MW

## Slide 14
GS’s Diameter: 970 [m]
Orbital Simulation (STK) - South Pole
South Pole Beam’s projection

## Slide 15
Orbital Simulation (STK)
N° Satellites: 3
Orbit Type: NRHO
Coverage: 100%
Mission from Earth (Astrogator)
Orbit Type: LLO

## Slide 16
Final Power Flux: 29.4 [W/m²]
Final Power Flux: 96.7 [W/m²]
Cost of Energy: 0.024 ÷ 0.013 [$/kWh]
Cost of Energy: ~ 0.011 [$/kWh]
Model Output - Ground Comparison
Noor Solar Park (Abu Dhabi)
Surface: 8 [km²]
Delivered Power: 1.18 [GW]
Average Heat Flux: 147 [W/m²]
Capacity Factor: 20 %
1 SPS Type 3 Satellite
Rectenna’s Surface: ~ 0.74 [km²]
Delivered Power: 1.18 [GW]
Average Heat Flux: 97 [W/m²]
Capacity Factor: 99.7 %
Operative Life: 25 years
Operative Life: 25 years

## Slide 17
Arash Safaei, Matteo D.L. Dalla Vedova, and Paolo Maggiore
Department of Mechanics and Aerospace Engineering (DIMEAS), Politecnico di Torino, Italy
“ Harnessing the Sun for the Moon: Thermo-Optical Analysis and Orbital Simulation of a Lunar Solar Power Satellite for Future Lunar Exploration”